# Tile Roof Proposal to Replace Underlayment

Gryphon Companies, Inc.			Office		480.994.5500

Roofing  Construction	Fax 		480.994.1189

P.O. Box 7309

Tempe, AZ 85281			Estimator:	Brooks Bryce

Licenses ROC #137-495 & 170-869, Bonded, and Insured	Mobile #:	602)327-2829

Proposal submitted to					Phone				Date

Heywood Realty – Attn: Leah			480-820-1519			August 30, 2010

Street							Work Address

42 S. Hamilton Pl. Suite 101			Discovery at Sunrise #1220

City, State, Zip Code					Work Address

Gilbert, AZ	85233				921 W. University Dr. #1220   Mesa, AZ

We hereby submit specifications and estimates for:

This proposal applies to 	replace underlayment on entire tile roof sections over unit #1220

1.  Remove & set aside tiles to be re-installed after underlayment is replaced.

2.  Remove all existing underlayment and wood battens down to a bare wood deck, haul away all debris.

3.  Remove & replace 1 sheet plywood, 6’ of 2”x 6” fascia and 8’ of 1”x 2” trim boards.

4.  Remove & replace additional rotten wood as necessary – see wood schedule attached(Terms & Conditions).

5.  Install new 	SBS modified 40# underlayment with a 6” overlap 	ELK TG-2

6.  Replace battens with new nominal 1 x 2 wood battens.

7.  Replace valley metal with 3-crown 26-gauge galvanized flashing.

8.  Replace all replaceable metal flashings.  Includes all vents, pipes, walls, chimney, skylight flashings.

9.  Install new 2”x 2” drip edge metal at eaves.       Brown  White  Galvanized

10.  Install bird-stop at eaves.    Black  Red

11.  Install hip and ridge enclosures at hips and at ridges.

12.  Replace **broken, cracked, or missing tiles, as needed.  **No extra charge for excessively broken tiles**	*Brand:      Lifetile	         *Color:  	Terra Cotta w/gold flash        *Style 	Concrete “S” Slurry

13.  Replace all mortar packs.

14.  Provide Five-year workmanship warranty against leaks.

* Tile will be matched to best of our ability, but we do not guarantee an exact match.	**Chipped tiles are not considered broken.

We Propose hereby to furnish material & labor -- complete in accordance with above specifications, for the sum of:

Two Thousand Eight Hundred Forty Five Dollars And 00/100	 $	2,845.00

Payment to be made as follows:					Sales tax  + 	   167.36

0	% down,  	100	 % upon completion.  	TOTAL $	3,012.36

Acceptance of Proposal:  These prices, specifications and conditions are satisfactory and are hereby accepted.

You are authorized to do the work as specified.  Payment will be made as outlined above.

Date of Acceptance

Signature manifests customer’s understanding & assent to the terms and conditions of Gryphon Co., Inc. on reverse.

Customer						Authorized

Signature 						Signature

Option:    Upgrade to a Peel-N-Stick rubber underlayment and a 10 year workmanship warranty against leaks		+ $ 600.00			 Initial to Accept